MMU STORAGE ASSEMBLY
Version 2024-04-19

---
TABLE OF CONTENTS
Introduction
04
Print Bed
138
Hardware Reference
07
StealthBurner
162
Wiring Prep
Frame
12
164
A/B Drive and Idler
22
Electronics
180
Controller Prep
Y Axis
40
202
Z Axis
62
Wiring
206
Skirts
X Axis
98
238
Belts
118
Panels
260

---
INTRODUCTION
THE MMU STORAGE PROJECT
This project is meant to be uses with an MMU like the ERCF (https://github.com/EtteGit/EnragedRabbitProject) and aims add on seamlessly to VORON printers design wise, while keeping your filament dry.
Currently this project has alpha status and is not fully finished. Some prototypes are built, but not all features are present or fully fledged out.
For Example future revision may use a heater to dry up already wet filament, therefore high temperature tolerant materials (e.g. polycarbonate instead of acrylic panels) are used. If the project deviates from that, it might switch to using acrylic panels.
ACKNOWLEDGMENTS
This project is heavily inspired by VORON DESIGN and even uses Parts from the VORON TRIDENT project (https://github.com/VoronDesign/Voron-Trident), namely:
STLs/Panels/bottom_panel_clip_x4.stl
STLs/Panels/bottom_panel_hinge_x2.stl
STLs/Panels/midspan_panel_clip_4mm_x7.stl
STLs/Panels/corner_panel_clip_4mm_x8.stl
STLs/Skirt/[a]_corner_baseplate_a_x2.stl
STLs/Skirt/[a]_corner_baseplate_b_x2.stl
STLs/Skirt/corner_a_x2.stl
STLs/Skirt/corner_b_x2.stl
This projects also heavily relies on the INTEGRATED AUTO-REWIND SPOOL HOLDER by VINCENT GROENHUIS (https://www.thingiverse.com/thing:3781815). Without this design, this project would not be possible!
Special Thanks to the VORON TEAM and VINCENT GROENHUIS for their awesome work!

---
INTRODUCTION
FILE NAMING
The STL file naming convention is the same as for VORON designs, namely:
PART PRINTING GUIDELINES
The print guidelines are also the same as for VORON designs, namely:
3D PRINTING PROCESS
Fused Desposition Modeling (FDM)
MATERIAL
ABS
LAYER HEIGHT
Recommended: 0.2mm
EXTRUSION WIDTH
Recommended: Forced 0.4mm
INFILL TYPE
Grid, Gyroid, Honeycomb, Triangle or Cubic
INFILL PERCENTAGE
Recommended: 40%
WALL COUNT
Recommended: 4
SOLID TOP/BOTTOM LAYERS
Recommended: 5
PRIMARY COLOR
Example z_joint_lower_x4.stl
These files will have nothing at the start of the filename.
ACCENT COLOR
Example [a]_tensioner_left.stl
We have added “[a]” to the front of any STL file that is intended to be printed with accent color.
QUANTITY REQUIRED
Example [a]_z_belt_clip_lower_x4.stl
If any file ends with “_x#”, that is telling you the quantity of that part required to build the machine.

---
INTRODUCTION
REPORTING ISSUES
Should you find an issue in the documentation or have a suggestion for an improvement please consider opening an issue on GitHub (https://github.com/Zergie/MMU-Filament-Storage/issues). When raising an issue please include the relevant page numbers and a short description; annotated screenshots are also very welcome. We periodically update the manual based on the feedback we get.
THIS IS JUST A REFERENCE
This manual is designed to be a simple reference manual. Building this project can be a complex endeavor and for that reason we recommend downloading the CAD files off our GitHub repository if there are sections you need clarification on. It can sometimes be easier to follow along when you have the whole assembly in front of you.

---
HARDWARE REFERENCE
BUTTON HEAD CAP BOLT (BHCS)
Metric fastener with a domed shape
head and hex drive. Most commonly
found in locations where M5 fasteners
are used.
ISO 7380-1
SOCKET HEAD CAP BOLT (SHCS)
Metric fastener with a cylindrical head
and hex drive. The most common
fastener used in this project.
ISO 4762
HEX NUT
Hex nuts couple with bolts to create a tight,
secure joint. You’ll see these used in both M3
and M5 variants throughout this guide.
ISO 4032
HEAT SET INSERT
Heat inserts with a soldering tip so that they melt the plastic when installed. As the plastic cools, it solidifies around the knurls and ridges on the insert for excellent resistance to both torque and pull-out.
POST INSTALL T-SLOT NUT (T-NUT)
Nut that can be inserted into the slot of
an aluminium profile. Used in M3, M4
and M5 variants throughout this guide.
Often also called “roll-in t-nut”.
608 BEARING
A ball bearing used on the auto rewind filament spools.
Adsadasd
asdasdasd
Adsadasd
asdasdasd

---
HARDWARE REFERENCE
BALL-END DRIVER
Some parts of this design require the use of a
ball-end hex driver for assembly. We recommend
you get a 2.0mm, 2.5mm and 3mm one.
2.5MM HEX DRIVER
The 2.5mm hex driver will see a lot of use in this
build. A quality driver is strongly recommended.
M5 TAP
Some extrusions need additional M5 threads. A tap with a tap handle will be needed. Be aware that for tapping aluminum you also need a lubricant for example tapping oil or WD40. Pre-tapped extrusions can also be used.
METAL DRILL BIT
Some extrusions also need access holes for the blind joints. A metal drill bit between 2-6 mm will work. Even not strictly necessary getting also a center punch can increase accuracy.

---
HARDWARE REFERENCE
BLIND JOINT BASICS
Blind Joints provide a cost effective and rigid assembly method.
The head of the BHCS is slid into the channel of another
extrusion and securely fastened through a small access hole in
the extrusion.
If you’ve never assembled one before we recommend you
watch the linked guide.
https://voron.link/onjwmcd

---
FRAME

---
FRAME
SORT EXTRUSIONS
Collect your extrusions and sort them by length.
We will highlight the extrusions used in each
step and label them as shown on this page
A Extrusion – 420mm Length
B Extrusion – 500mm Length
C Extrusion - 200mm Length
B Extrusion
A Extrusion
C Extrusion

---
FRAME
10MM Drill Guide
For blind joint access holes
located at the edge of the B
extrusions.
233MM Drill Guide
For the upper drawer support
blind joint access holes located
on the B extrusions.

---
FRAME
B Extrusion
DRILL ACCESS HOLES
Drill access holes for the blind
joint 10mm from the edge of
the extrusion.
DRILL ACCESS HOLES
Drill access holes for the blind
joint 233mm from the left edge of
the extrusion
DRILL ACCESS HOLES
Drill access holes for the blind
joint 10mm from the edge of
the extrusion.

---
FRAME
TAP M5
Tap both ends of the extrusion
for a M5 screw.
C Extrusion

---
M5x16 BHCS
FRAME
Blind Joint Plugs
BLIND JOINT PLUGS
To keep as much moisture out as possible, we
need to plug all blind joints. These plugs do fit
very tightly and need some force
MIND THE ORIENTATION
The extrusions are going to be used in this
section. Prepare them as shown above.
Mind the orientation of the center hole.
B Extrusion
ONLY TWO BLIND JOINT PLUGS
Mind to install only two Blind Joint
Plugs here.

---
FRAME
ALIGN COMPONENTS
Align Blind Joint Plugs and Screws
as shown above.

---
FRAME
B Extrusion
BUILD ON A FLAT SURFACE
Build the frame on a glass or granite surface
to ensure you can get it as square as possible.
MIND BLIND JOINTS
We do our best to call out things that may bite
you later in the assembly process but may
skip things that seem obvious to us. If in doubt
please refer to the CAD model, it might save
you some considerable time down the road.
C Extrusion
Back
FIRST BLIND JOINT
This design relies on blind joints to
assemble the frame. We outlined
the basics of blind joints on page 7
.
If you’ve never assembled one
before we recommend you watch
the linked guide.
https://voron.link/onjwmcd

---
FRAME
Back

---
FRAME
B Extrusion
Back

---
FRAME
C Extrusion
C Extrusion
C Extrusion
Back
Back

---
FRAME
B Extrusion
B Extrusion
Back

---
FRAME
Back

---
FRAME
COVER BLIND JOINT ACCESS
Cover up all Blind Joint screws with the Blind
Joint Plates.
Back

---
FRAME
Top
Top
CHECK FOR SQUARENESS
Verify the angle of all corners and the
overall squareness by measuring the
diagonals. Refer to the second half of the
linked video for additional information.
https://voron.link/kdtpzam

---
DRAWER

---
FEET

---
DECK PANEL

---
DIN RAILS

---
SKIRTS

---
BOTTOM PANEL

---
PANELS

---
MMU STORAGE
WEBSITE
GITHUB
https://github.com/Zergie/MMU-Filament-Storage