MMU STORAGE ASSEMBLY
Version 2024-04-05

---
TABLE OF CONTENTS
Introduction
04
Print Bed
138
Hardware Reference
07
StealthBurner
162
Wiring Prep
Frame
12
164
A/B Drive and Idler
22
Electronics
180
Controller Prep
Y Axis
40
202
Z Axis
62
Wiring
206
Skirts
X Axis
98
238
Belts
118
Panels
260

---
INTRODUCTION
THE MMU STORAGE PROJECT
This project is meant to be uses with an MMU like the ERCF (https://github.com/EtteGit/EnragedRabbitProject) and aims add on seamlessly to VORON printers design wise, while keeping your filament dry.
Currently this project has alpha status and is not fully finished. Some prototypes are built, but not all features are present or fully fledged out.
For Example future revision may use a heater to dry up already wet filament, therefore high temperature tolerant materials (e.g. polycarbonate instead of acrylic panels) are used. If the project deviates from that, it might switch to using acrylic panels.
ACKNOWLEDGMENTS
This project is heavily inspired by VORON DESIGN and even uses Parts from the VORON TRIDENT project (https://github.com/VoronDesign/Voron-Trident), namely:
STLs/Panels/bottom_panel_clip_x4.stl
STLs/Panels/bottom_panel_hinge_x2.stl
STLs/Panels/midspan_panel_clip_4mm_x7.stl
STLs/Panels/corner_panel_clip_4mm_x8.stl
STLs/Skirt/[a]_corner_baseplate_a_x2.stl
STLs/Skirt/[a]_corner_baseplate_b_x2.stl
STLs/Skirt/corner_a_x2.stl
STLs/Skirt/corner_b_x2.stl
This projects also heavily relies on the INTEGRATED AUTO-REWIND SPOOL HOLDER by VINCENT GROENHUIS (https://www.thingiverse.com/thing:3781815). Without this design, this project would not be possible!
Special Thanks to the VORON TEAM and VINCENT GROENHUIS for their awesome work!

---
INTRODUCTION
FILE NAMING
The STL file naming convention is the same as for VORON designs, namely:
PART PRINTING GUIDELINES
The print guidelines are also the same as for VORON designs, namely:
3D PRINTING PROCESS
Fused Desposition Modeling (FDM)
MATERIAL
ABS
LAYER HEIGHT
Recommended: 0.2mm
EXTRUSION WIDTH
Recommended: Forced 0.4mm
INFILL TYPE
Grid, Gyroid, Honeycomb, Triangle or Cubic
INFILL PERCENTAGE
Recommended: 40%
WALL COUNT
Recommended: 4
SOLID TOP/BOTTOM LAYERS
Recommended: 5
PRIMARY COLOR
Example z_joint_lower_x4.stl
These files will have nothing at the start of the filename.
ACCENT COLOR
Example [a]_tensioner_left.stl
We have added “[a]” to the front of any STL file that is intended to be printed with accent color.
QUANTITY REQUIRED
Example [a]_z_belt_clip_lower_x4.stl
If any file ends with “_x#”, that is telling you the quantity of that part required to build the machine.

---
INTRODUCTION
REPORTING ISSUES
Should you find an issue in the documentation or have a suggestion for an improvement please consider opening an issue on GitHub (https://github.com/Zergie/MMU-Filament-Storage/issues). When raising an issue please include the relevant page numbers and a short description; annotated screenshots are also very welcome. We periodically update the manual based on the feedback we get.
THIS IS JUST A REFERENCE
This manual is designed to be a simple reference manual. Building this project can be a complex endeavor and for that reason we recommend downloading the CAD files off our GitHub repository if there are sections you need clarification on. It can sometimes be easier to follow along when you have the whole assembly in front of you.

---
HARDWARE REFERENCE
BUTTON HEAD CAP BOLT (BHCS)
Metric fastener with a domed shape
head and hex drive. Most commonly
found in locations where M5 fasteners
are used.
ISO 7380-1
SOCKET HEAD CAP BOLT (SHCS)
Metric fastener with a cylindrical head
and hex drive. The most common
fastener used in this project.
ISO 4762
Adsadasd
asdasdasd
Adsadasd
asdasdasd
Adsadasd
asdasdasd
Adsadasd
asdasdasd
Adsadasd
asdasdasd
Adsadasd
asdasdasd

---
HARDWARE REFERENCE
BLIND JOINT BASICS
Blind Joints provide a cost effective and rigid assembly method.
The head of the BHCS is slid into the channel of another
extrusion and securely fastened through a small access hole in
the extrusion.
If you’ve never assembled one before we recommend you
watch the linked guide.
https://voron.link/onjwmcd

---
FRAME

---
SORT EXTRUSIONS
Collect your extrusions and sort them by length.
We will highlight the extrusions used in each
step and label them as shown on this page
A Extrusion – 420mm Length – 0 Holes
B Extrusion – 500mm Length – 8 Holes
C Extrusion - 200mm Length – 2 Holes
D Extrusion - 200mm Length – 4 Holes
E Extrusion – 460mm Length – 0 Holes
B Extrusion
E Extrusion
A Extrusion
C Extrusion
D Extrusion

---
M5x16 BHCS
M5x16 BHCS
A Extrusion
D Extrusion
C Extrusion
M5x16 BHCS
M5x16 BHCS
PREPARE A EXTRUSIONS
The extrusions are going to be used in this
section. Prepare them as shown above.

---
B Extrusion
ADD BLIND JOINT PLUGS
To keep as much moisture out as possible, we
need to plug all blind joints. Add the plugs to
all inside corners as shown below. Continue
doing this for all joints.
C Extrusion
A Extrusion
A Extrusion
Back

---
B Extrusion
BUILD ON A FLAT SURFACE
Build the frame on a glass or granite surface
to ensure you can get it as square as possible.
ADD BLIND JOINT PLUGS
To keep as much moisture out as possible, we
need to plug all blind joints. Add the plugs to
all inside corners as shown below. Continue
doing this for all joints.
C Extrusion
A Extrusion
A Extrusion
MIND ACCESS HOLE POSITION
We do our best to call out things that may bite
you later in the assembly process but may
skip things that seem obvious to us. If in doubt
please refer to the CAD model, it might save
you some considerable time down the road.
FIRST BLIND JOINT
This design relies on blind joints to
assemble the frame. We outlined
the basics of blind joints on page 7
.
If you’ve never assembled one
before we recommend you watch
the linked guide.
https://voron.link/onjwmcd
Back

---
SECOND CORNER
Build the second corner.
Don’t forget the Blind Joint Plugs.
B Extrusion
D Extrusion
Back

---
ADD MIDDLE SUPPORT
Build the middle support. Do not tighten just
yet.
TODO: Add new Blind Joint Plugs
A Extrusion
Back

---
A Extrusion
Back